## Slide 1
A Novel Method of Oligonucleotide Detection using Diels Alder Cycloaddition and SERRS
Ljiljana Fruk,Duncan Graham and W. Ewen Smith ljiljana.fruk@strath.ac.uk
Department of Pure and Applied Chemistry, University of Strathclyde, Glasgow G1 1XL
Diels Alder Cycloaddition of the Dye to Oligonucleotide
in phosphate buffer (pH = 5.5)2, 30%CH3CN, 40C
cycoaddition was followed by HPLC:
Detection by SERRS
SERRS surface has to be rough, resistant to the harsh conditions, stable with time and give reproducible SERRS
Introduction
With the completion of the human genome project, a growing number of scientists are trying to use the information to find a way of identifying genetic diseases linked to alternations in DNA. This requires screening of different DNA sequences for specific sequence characteristics in a high throughput manner. In modern DNA analysis fluorescent labelling is the most favoured DNA detection technique1. However, addition of fluorescent labels can be disadvantageous since most of these dyes have appreciable biological activity, which leads to reduced activity or even total inactivity of the probe. Here we present a novel, convenient method of DNA labelling in an aqueous environment and detection by SERRS.
Surface Enhanced Resonance Raman Scattering
requires adsorbtion of the species on the metal surface
active species have chromophores that match the laser excitation frequency
(visible laser usually used)
fluorescence is quenched
detection limits lowered compared to other techniques
Diels Alder cycloaddition
SERRS active dienophile
consists of:
1) the benzotriazole group for surface attachment
2) the chromophore
3) the maleimide group to undergo Diels Alder reaction
Oligonucleotide diene
12 base synthetic oligo used - 5’TCTCAACTCGTA
Chemiclly modified with furan via amino link
Biologically important molecules including DNA are not SERRS active and have to be labelled with SERRS active species prior to detection.
Diels Alder cycloaddition used to attach coloured species to oligo
diene
cycloadduct
Dienophile
+
Not SERRS active (oligo)
SERRS active (benztriazole dye)
SERRS active oligo
DCM
2.
1. CDI, DMF
+
BT maleimide
Oligo furan
Oligo cycloadduct
1 BT maleimide
2 Oligo cycloadduct
PVA discs3
Ag NO3 in polvinylalcohol (PVA) solution (5% in H2O), spin coated on the glass discs,
dried and reduced with saturated FeSO4 solution.
SERRS maps done to check the reproducibility of the signal over the larger area of the substrate–BT maleimide adsorbed on the surface used.
Surface mapping image
3D representation
Detection of modified oligo
514 nm
laser
PVA disc
Oligo cycloadduct
BT dye maleimide
oligo cycloadduct gave spectra which differed form the spectra of dye maleimide
Conclusions
specific BT dye maleimide was designed to label oligonucleotide
oligo was successfully labelled with SERRSactive dye using Diels Alder reaction- different dyes can be designed therefore leading to many different labels
Cycloadditon can be followed both by HPLC and SERRS
SERRS spectra of dye maleimide differes from spectra of oligo cycloadduct enabling the analysis of the oligo in situ and in the presence of the starting material
3 accumulations, 3sec
References
1. P.Zhang, T. Beck, W. Tan, Angew.Chem.Int.Ed., 2001,40 (2),402-406
2. K. W. Hill et al., J.Org.Chem., 2001, 66, 5352-5358
3. M. Volkan, D. L. Stokes, T. Vo-Dinh, Appl. Spec., 2000, 54(12), 1842-1848.