## Slide 1
A Novel Method of Oligonucleotide Detection Using Diels Alder Cycloaddition and SERRS
Ljiljana Fruk, Duncan Graham, W. Ewen Smith

## Slide 2
Post human genome era
identification of genetic diseases
Screening of large number of DNA sequences – DNA arrays (fluorescence used)
Problems
Complex chemistry,
biological activity
Separation of a label and labelled oligo prior to detection

## Slide 3
Solution:
Surface Enhanced Resonance Raman Scattering?

## Slide 4
Raman scattering
ho
ho
Rayleigh scattering
ho  1
Raman scattering
Vibrational spectroscopy
Weak process

## Slide 5: Surface Enhanced Resonance Raman Spectroscopy
Surface enhancement
molecule adsorbed on a roughened surface
large increase in signal
signal sensitive to the orientation of a ligand
Resonance Raman
laser frequency coincides or approaches the frequency of an electronic transition

## Slide 6
Biologically important molecules including DNA are not SERRS active and have to be labelled with SERRS active species prior to detection.
Surface Enhanced Resonance Raman Scattering
requires adsorption of the species on the metal surface
active species have chromophores that match the laser excitation frequency (visible laser usually used)
fluorescence is quenched
detection limits lowered compared to other techniques

## Slide 7
DNA has to be labelled with SERRS active species
Diels Alder cycloaddition
diene
cycloadduct
Dienophile
+
Not SERRS active (oligo)
SERRS active (benzotriazole dye)
SERRS active oligo

## Slide 8
, DCM
1.
2. Co naphthenate, Ac2O
SERRS active dienophile*
consists of:
1) the benzotriazole group for surface attachment
2) the chromophore – azo group
3) the maleimide group to undergo Diels Alder reaction
*Lj. Fruk, A. Grondin, D. Graham, E. W. Smith: A New Approach to Oligonucleotide Labelling Using Diels Alder Cycloadditons and SERRS, Chemn. Comm.,2002, 18,2100-2101

## Slide 9
DCM
2.
CDI, DMF
Oligonucleotide diene
12 base synthetic oligo used - 5’TCTCAACTCGTA
modified with furan via amino link
Lj. Fruk, A. Grondin, D. Graham, E. W. Smith: A New Approach to Oligonucleotide Labelling Using Diels Alder Cycloadditons and SERRS, Chemn. Comm.,2002, 18,2100-2101

## Slide 10
+
1 Oligo furan
2 Oligo cycloadduct
Diels Alder Cycloaddition of the Dye to Oligonucleotide
in phosphate buffer (pH = 5.5), 30% CH3CN, 40C
HPLC trace

## Slide 11
Ag -PVA disc

## Slide 12: SERRS substrates
Mainly used:
silver colloid
reproducibility in the short period of
time (ageing)
cold deposited silver films
roughness lost with time
surface susceptible to damage

## Slide 13
Protein and DNA arrays
Surface has to be rough, resistant to the assay conditions, stable with time and give reproducible SERRS

## Slide 14
Ag-PVA discs
Ag NO3 in polyvinylalcohol (PVA) solution (5% in H2O),
spin coated on the glass discs, dried and reduced with saturated FeSO4 solution.
SERRS maps done to check the reproducibility of the signal over the larger area of the substrate. BT maleimide dye adsorbed on the surface

## Slide 15
Surface mapping image
3D map
514 nm laser
3 accum, 3 sec
400x400 m

## Slide 16
Electron Microprobe Analysis (EMPA)
similar in design to SEM, but better for analysis of light elements
Cameca SX100 instrument
3 WDS and 1 EDS
spectrometer
Secondary electron image of Ag-PVA disc

## Slide 17
Ag map, 15kV,10nA
O map, 15kV, 10 nA
Silver and oxygen maps performed
- no iron found (good!)

## Slide 18
SERRS map of a damaged disc
514 nm

## Slide 19
Conclusions:
BT dye maleimide designed
Novel SERRS active substrates characterised
Oligo successfully labelled with SERRS active dye
SERRS spectra of dye maleimide differs from spectra of oligo cycloadduct enabling the analysis of the oligo in situ and in the presence of the starting material without separation

## Slide 20
Acknowledgments
Inspiration
Prof. W. E. Smith
Dr. Duncan Graham
“Chemistry is largely experimental science”
Dr. Antonio Grondin
Dr. Robert Martin
Prof. Andrew Mills
Callum McHugh
Rachel Brown
Alexis Enright
Both Inorganic and Raman Groups at the University
Ideas
Fun
Facts
Notes: afaskdjsaoda