## Slide 1
A Novel Approach to DNA Detection using SERRS
Ljiljana Fruk

## Slide 2
Post human genome era
identification of genetic diseases
Screening of large number of DNA sequences – DNA arrays (fluorescence used)
Problems
Complex chemistry,
reduced biological activity
Separation of a label and labelled oligo prior to detection

## Slide 3
Solution:
Surface Enhanced Resonance Raman Scattering?

## Slide 4
Biologically important molecules including DNA are not SERRS active and have to be labelled with SERRS active species prior to detection.
Surface Enhanced Resonance Raman Scattering
requires adsorption of the species on the metal surface
active species have chromophores that match the laser excitation frequency (visible laser usually used)
fluorescence is quenched
detection limits lowered compared to other techniques

## Slide 5
DNA has to be labelled with SERRS active species
Diels Alder cycloaddition
diene
cycloadduct
Dienophile
+
Not SERRS active (oligo)
SERRS active (benzotriazole dye)
SERRS active oligo

## Slide 6
, DCM
1.
2. Co naphthenate, Ac2O
SERRS active dienophile*
consists of:
1) the benzotriazole group (BT) for surface attachment
2) the chromophore – azo group
3) the maleimide group to undergo Diels Alder reaction
4 different BT dye maleimides synthesised

## Slide 7
DCM
2.
CDI, DMF
Oligonucleotide diene
12 base synthetic oligo used - 5’TCTCAACTCGTA
modified with furan via amino link
modifed with butadiene phosphoramidate during automated synthesis

## Slide 8
+
1 Oligo furan
2 Oligo cycloadduct
Diels Alder Cycloaddition of the Dye to
Oligonucleotide
in phosphate buffer (pH = 5.5), 30% CH3CN, 40C
HPLC trace

## Slide 9
Ag -PVA disc
SERRS Detection of Labelled Oligos
Detected in 10-17 moles

## Slide 10
Different spectra obtained when different dienes used with the same dye maleimide – great possibilities for multiplexing
BT dye maleimide
Oligo furan
Oligo butadiene

## Slide 11: SERRS substrates
Mainly used:
silver colloid
reproducibility in the short period of
time (ageing)
cold deposited silver films
roughness lost with time
surface susceptible to damage

## Slide 12
Ag-PVA discs
Ag NO3 in polyvinylalcohol (PVA) solution (5% in H2O),
spin coated on the glass discs, dried and reduced with saturated FeSO4 solution.
SERRS maps done to check the reproducibility of the signal over the larger area of the substrate. BT maleimide dye adsorbed on the surface

## Slide 13
3D map
514 nm laser
3 accum, 3 sec, 400x400 m
PVA-Ag surface additionally investigated by Electron Microprobe – elemental analysis of the surface.

## Slide 14
SERRS beacons
ONE RING TO BIND THEM, ONE RING TO RULE THEM ALL

## Slide 15
Molecular Beacons
Q
R
R
Q
R
Q
R
Q
R
Q
Q
R
Q
R
Problem: residual fluorescence due to the insufficient quenching
Quenchers (azo dyes): DABCYL, BHQ
Application in genetics, disease diagnostics, new drug development

## Slide 16
SERRS Beacons
Q
R
R
Q
R
Q
R
Q
Q
R
R
Q
Q
R
Bt dyes excellent quenchers, silver nanoparticles contribute additionally to the quenching.

## Slide 17
SERRS beacon
Closed beacon on the Ag surface
target DNA

## Slide 18
control
single base mismatch
SERRS beacon in the presence of control and single base mismatched oligo.
Excellent specificity for target DNA, range of SERRS dyes available for labelling, many possible quencher-flurophore pairs.

## Slide 19
Conclusions:
Novel SERRS active substrates characterised
Oligo successfully labelled with SERRS active dye and detected at 10-17 moles
SERRS spectra of dye maleimide differs from spectra of oligo cycloadduct enabling the analysis of the oligo in situ and in the presence of the starting material without separation
AND THE MOST IMPORTANT:
SERRS molecular beacons designed enabling the new advances in biotechnology

## Slide 20
Ljiljana
10 things to know about Croatia
1230 island
7 National Parks
15 Top Models at the moment
Successful in sport (football, handball, skiing, waterpolo champions)
Two Nobel Prize Winners in Chemistry
One Wimbeldon Winner
The Home country of the Tie
Home of Goran Visnjic
Leading centre for animated movies
Home of excellent cuisine
Notes: afaskdjsaoda